Exam Ref 70-740 Installation, Storage, and Compute with Windows Server 2016

First Edition

Copyright © 2017 Pearson Education, Inc.

ISBN-10: 0-735-69882-1
ISBN-13: 978-0-7356-9882-6

Warning and Disclaimer

Every effort has been made to make this book as complete and as accurate as possible, but no warranty or fitness is implied. The information provided is on an "as is" basis. The author and the publisher shall have neither liability nor responsibility to any person or entity with respect to any loss or damages arising from the information contained in this book or from the use of the CD or programs accompanying it.

When reviewing corrections, always check the print number of your book. Corrections are made to printed books with each subsequent printing.

First Printing: January 2017

Corrections, June 12, 2019

| Pg | Error | Correction |
| --- | --- | --- |
| 144 | Third last line, Para 3, Reads: The Algorithm parameter specifies which of two transmission selection algorithms, EBS or Strict, defined in the DCB standard the traffic class should use. | Should read: The Algorithm parameter specifies which of two transmission selection algorithms, ETS or Strict, defined in the DCB standard the traffic class should use. |

Corrections, March 22, 2018, 5th printing

| Pg | Error | Correction |
| --- | --- | --- |
| 77 | 3rd row of table from bottom of page Reads: Disable-W.indowsOptionalFeature | Should read: Disable-WindowsOptionalFeature |
| 162 | Bottom, 2nd bullet, 2nd sentence: Reads: You can create image files using VHD or the newer VHDX format with the Disk Management snap-in or the Get-VHD cmdlet in Windows PowerShell. | Should read: You can create image files using VHD or the newer VHDX format with the Disk Management snap-in or the New-VHD cmdlet in Windows PowerShell. |
| 163 | Top of page, 5th bullet: Tiered storage is a feature of virtual that uses faster SSD drives in a storage pool to store the most frequently used files. | Should read Tiered storage is a feature of virtual disks that uses faster SSD drives in a storage pool to store the most frequently used files. |
| 257 | 3rd bullet from bottom of page: Reads: NIC teaming a technique for aggregating the bandwidth of multiple network adapters, to provide improved performance and fault tolerance. | Should read: NIC teaming is a technique for aggregating the bandwidth of multiple network adapters, to provide improved performance and fault tolerance. |
| 269 | Top first block of code Reads: { "graph": "d:\\docker" "bridge" : "none" "group" : "docker" {"dns": 192.168.9.2, 192.168.9.6 } } | Should read: { "graph": "d:\\docker", "bridge" : "none", "group" : "docker", {"dns": 192.168.9.2, 192.168.9.6 } } |
| 281 | Bottom paragraph, currently reads: The container is 172.25.117.12/12 | Should read: The container is 172.25.117.12/20 |
| 282 | First paragraph, currently reads: The other adapter has the address 172.25.112.1/12 | Should read: The other adapter has the address 172.25.112.1/20 |
| 282 | Frist paragraph, currently reads: The container host is, in essence, functioning as a router between the 172.16.0.0/12 network | Should read: The container host is, in essence, functioning as a router between the 172.25.112.0/20 network |
| 283 | First words on page, currently reads: 172,25.117.12 address | Should read: 172.25.117.12 address |
| 282 | Second paragraph, currently reads: as well as those of systems outside the 172.16.0.0/12 network. | Should read: as well as those of systems outside the 172.25.112.0/20 network. |
| 283 | First full paragraph, currently reads: The use of the 172.16.0.0/12 network address | Should read: The use of the 172.25.112.0/20 network address |
| 397 | Chapter 6 missing figure above Exam Tip and after first paragraph | Figure 6.8 needs to be inserted, with caption. |

Corrections, January 19, 2018, 4th printing

| Pg | Error | Correction |
| --- | --- | --- |
| 3 | 4th bullet under “Minimum hardware requirements” Network adapter: Ethernet, with gigabit throughout | Change to: Network adapter: Ethernet, with gigabit throughput |
| 19 | Heading: Configuring Server Core above bulleted list at bottom. |  |
| 32 | 1st bulleted item “Between versions” You can migrate data from any Windows Server version since Windows Server 2003 SP2 to Windows Server 2016. This includes migrations from one server running Windows Server 2016 to another. | Change to: You can migrate data from any Windows Server version since Windows Server 2008 to Windows Server 2016. This includes migrations from one server running Windows Server 2016 to another. |
| 86 | 3rd paragraph from top The GPT disk partitioning style supports volumes up to 18 exabytes (1 exabyte = 1 billion gigabytes, or 260 bytes). | Change to: The GPT disk partitioning style supports volumes up to 18 exabytes (1 exabyte = 1 billion gigabytes, or 260 bytes). |
| 94 | Paragraph starting with “ReFS (Resilient File System)” The maximum ReFS volume size is 280 bytes, or 1 yobibyte | Change to: The maximum ReFS volume size is 280 bytes, or 1 yobibyte. |
| 134 | Last line of page (code line): install-windowsfeature -name fs-iscsitarget-server -installmanagementtools | Change to: install-windowsfeature -name fs-iscsitarget-server -includemanagementtools |
| 143 | Bottom, sentence above single code line: To set the DCBX Willing bit to false, you use the Set-NetQoSbcdxSetting cmdlet, as in the following example: | Change to: To set the DCBX Willing bit to false, you use the Set-NetQoSdcbxSetting cmdlet, as in the following example: |
| 144 | Subheading “Create QoS Policies,” second to last bulleted item IpDstMatchCondition Filters traffic based on a specific destination port number | Change to: IPDstPortMatchCondition Filters traffic based on a specific destination port number |
| 153 | 1st paragraph Then, the cmdlet runs performance tests for a time interval that you specify in the command line. The ideal way to run this test is while the source server is running under its usual workload. The test proceeds to measure the synchronization performance between the source and the destination, to determine if the throughout is sufficient for synchronous replication, and presents the results in a chart, as shown in Figure 2-57. | Change to: Then, the cmdlet runs performance tests for a time interval that you specify in the command line. The ideal way to run this test is while the source server is running under its usual workload. The test proceeds to measure the synchronization performance between the source and the destination, to determine if the throughput is sufficient for synchronous replication, and presents the results in a chart, as shown in Figure 2-57. |
| 169 | Text in 2nd bullet Hardware-enforced Data Execution Prevention (DEP), which Intel describes as eXecute Disable (XD) and AMD describes as No eXecute (NS). CPUs use this technology to segregate areas of memory for either storage of processor instructions or for storage of data. Specifically, you must enable Intel XD bit (execute disable bit) or AMD NX bit (no execute bit). | Change to: Hardware-enforced Data Execution Prevention (DEP), which Intel describes as eXecute Disable (XD) and AMD describes as No eXecute (NX). CPUs use this technology to segregate areas of memory for either storage of processor instructions or for storage of data. Specifically, you must enable Intel XD bit (execute disable bit) or AMD NX bit (no execute bit). |
| 173 | 2nd paragraph under heading, “Upgrade from existing versions of Hyper-V” The first step in upgrading a host server to Windows Server 2016 is to get the virtual machines off the host, for their own protection. You can do this in two ways: | Change to: The first step in upgrading a host server to Windows Server 2016 is to get the virtual machines off the host, for their own protection. You can do this in three ways: |
| 210 | Line of code under Figure 3-34 export-vm -name server1 -path c\export | Change to: export-vm -name server1 -path c:\export |
| 228 | Last code line above subheading, “Manage checkpoints” merge-vhd -path c:\disks\child.vhdx -destionationpath c:\disks\parent.vhdx | Change to: merge-vhd -path c:\disks\child.vhdx -destinationpath c:\disks\parent.vhdx |
| 261 | Last sentence, 1st paragraph under “Install and Configure….” Heading Windows Server Containers operate user mode and share everything with the host computer, including the operating system kernel and the system memory. | first para in Install and Configure section - sentence should read: Windows Server Containers operate in user mode and share everything with the host computer, including the operating system kernel and the system memory. |
| 263 | Text in 2nd bullet: Hardware-enforced Data Execution Prevention (DEP), which Intel describes as eXecuted Disable (XD) and AMD describes as No eXecute (NS). CPUs use this technology to segregate areas of memory for either storage of processor instructions or for storage of data. Specifically, you must enable Intel XD bit (execute disable bit) or AMD NX bit (no execute bit). | Change to: Hardware-enforced Data Execution Prevention (DEP), which Intel describes as eXecuted Disable (XD) and AMD describes as No eXecute (NX). CPUs use this technology to segregate areas of memory for either storage of processor instructions or for storage of data. Specifically, you must enable Intel XD bit (execute disable bit) or AMD NX bit (no execute bit). |
| 267 | Step 2 under “Installing Docker on Nano Server To enable the Dockerd engine to accept client traffic over the network, you must create a text file called daemon.json in the C:\ProgramData\Docker directory on the Nano Server that contains the following line: | Change to: To enable the Dockerd engine to accept client traffic over the network, you must create a text file called daemon.json in the C:\ProgramData\Docker\config directory on the Nano Server that contains the following line: |
| 287 | 2nd sentence under heading, “Manage resource control” For example, you have seen how the it switches create an interactive container that runs a specific shell or other command. | Change to: For example, you have seen how the -it switches create an interactive container that runs a specific shell or other command. |
| 306 | 3rd line of code from the top of page Set-VMHost -VirtualMachineMigrationAuthenticatiuonType Kerberos | Change to: Set-VMHost -VirtualMachineMigrationAuthenticationType Kerberos |
| 340 | Last line of code at bottom of page -continuouslyavailable set-smbpathacl –sharename share1 | Change to: -continuouslyavailable set-smbpathacl –sharename share1 |
| 344 | Step 10. On the Specify The Size Of TThe Virtual Disk page, type a size in MB, GB, or TB, or select the Maximum Size checkbox. | Change to: On the Specify The Size Of The Virtual Disk page, type a size in MB, GB, or TB, or select the Maximum Size checkbox. |
| 354 | Subheading, “Enable Storage Spaces direct using Windows PowerShell,” 3rd paragraph The storage will be added when you enable Stoage Spaces Direct. | Change to: The storage will be added when you enable Storage Spaces Direct. |
| 354 | section heading Enable Storage Spaces direct using Windows PowerShell | Change to: Enable Storage Spaces Direct using Windows PowerShell |
| 360 | Last sentence of 1st paragraph under “Continuously available share settings” Both roles enable you to create shares that are continuously available through the use the SMB 3.0 protocol. | Change to: Both roles enable you to create shares that are continuously available through the use of the SMB 3.0 protocol. |
| 368 | Last bulleted item above “Skill 5.5: Manage VM movement in clustered nodes” 3 High. Migrates VMs when the host is more than 60 perecnt loaded. | Change to: High. Migrates VMs when the host is more than 60 percent loaded. |
| 373 | 4th paragraph from the top: To import the virtual machine into the Hyper-V host, copy the files to the host’s default folders and generating a new security identifier (SID) for the VM. , To prevent conflicts, use a command like the following: | Change to: To import the virtual machine into the Hyper-V host, copy the files to the host’s default folders and generate a new security identifier (SID) for the VM. To prevent conflicts, use a command like the following: |
| 388 | 3rd bullet on page (Compliance bullet): The default Windows Update configuration provides no means for administrators to confirm that the client has successfully installed all the required updates successfully, except to examine the Update History on each computer individually. | Change to: The default Windows Update configuration provides no means for administrators to confirm that the client has installed all the required updates successfully, except to examine the Update History on each computer individually. |
| 393 | Last line on page (a code line): wsusutil.exe postinstall sql_instance_name="db1\sqlinstance1 content_dir=d:\wsus | Change to: wsusutil.exe postinstall sql_instance_name="db1\sqlinstance1" content_dir=d:\wsus |
| 393 | First sentence, 2nd paragraph under heading “Deploying WSUS” WSUS is a just local version of a Microsoft Update server, so it needs a web server to which clients can connect. | Change to: WSUS is just a local version of a Microsoft Update server, so it needs a web server to which clients can connect. |
| 396 | Step 7 (no content) | Delete “7.” |

Correction for February 24, 2017

| Pg | Error – First Printing | Correction |
| --- | --- | --- |
| 5 | Bottom, in NOTE UNDERSTANDING OSES Microsoft now uses the term operating system environment (OSE) to refer to the Windows instances running on a computer. An OSE can be physical or virtual. For example, a server running one virtual machine in Hyper-V would be using two OSEs because the physical server installation counts for one. The Standard edition license therefore enables you to run one virtual machine in Hyper-V. | Change to Microsoft now uses the term operating system environment (OSE) to refer to the Windows instances running on a computer. An OSE can be physical or virtual. For example, a server running one virtual machine in Hyper-V would be using two OSEs because the physical server installation counts for one. |
| 10 | Top of page, last line in the 'format' section. "You do not need to format any new partitions you create for the install, but you might want to format an existing partition to eliminate unwanted files before installing Windows Server 2012 R2 on it." | Change to: “You do not need to format any new partitions you create for the install, but you might want to format an existing partition to eliminate unwanted files before installing Windows Server 2016 on it." |
| 25 | 2nd paragraph from bottom For example, you can use the Event Viewer console on a full GUI Windows installation to connect a computer running Server Core and view its logs. | For example, you can use the Event Viewer console on a Desktop Experience Windows installation to connect a computer running Server Core and view its logs. |
| 94 | Bottom ReFS disks also cannot be read by any operating systems older than Windows Server 2012 R2 and Windows 8 | Change to: ReFS disks also cannot be read by any operating systems older than Windows Server 2012 and Windows 8.1. |

This errata sheet is intended to provide updated technical information. Spelling and grammar misprints are updated during the reprint process, but are not listed on this errata sheet.